## Slide 1
01 · THE PROBLEM
LiDAR - Camera Fusion Robustness in Adverse Weather
Autonomous driving detectors fail 20 - 40% in rain, fog and snow, especially at oblique angles (90°, 180° azimuth). The degradation is angle-dependent and not well understood.
ANGLE-DEPENDENT FAILURE
20 - 40%
detection failure in rain, fog and snow - worst at 90° and 180° azimuth.
RESEARCH QUESTION
“How does adverse weather affect LIDAR-camera fusion perfomance across different observations angles, and can combined fusion models improve robustness?”
AZIMUTH
0°, 45°, 90°, 180° azimuth
Clear, rain, fog, night
Oblique angles (90°, 180°) degrade worst
Notes: Autonomous driving detectors fail 20-40% in rain, fog and snow, especially at oblique angles. The degradation is angle-dependent and not well understood. That is the gap this dissertation addresses.

## Slide 2
02 · SOLUTION
Phase 1: measure how accuracy varies, using pre-trained models
Using pre-trained 3D object detection models to measure how detection accuracy varies by angle, weather and dataset - then combining two pre-trained models.
PHASE 1 · WHAT VARIES
Angle, weather, datasets
Angle - 0°, 45°, 90°, 180° (azimuth)
Weather - clear, rain, fog, night
Datasets - nuScenes (primary), Ithaca365 (validation), CADC (snow)
MODEL 1 · ECCV 2024
SAMFusion - good for bad conditions
Deep learning model designed specifically for adverse weather.
Explicitly trained on rain / fog / snow scenarios
Sensor-adaptive: learns which sensor to trust when
Pre-trained weights available (Princeton CI Lab)
Robust in bad weather
MODEL 2 · ICRA 2023
BEVFusion - accuracy
Industry-standard 3D object detection model.
Production-proven
High accuracy in clear weather
Pre-trained weights available (NVIDIA NGC)
Pre-trained on nuScenes clear weather
Notes: Phase 1 uses pre-trained 3D object detection models to measure how detection accuracy varies by angle, weather and dataset. Two pre-trained models are combined: SAMFusion for bad conditions, BEVFusion for accuracy.

## Slide 3
03 · STRATEGY
Run both models, combine their predictions
Combined
SCENARIO
SAMFUSION ALONE
BEVFUSION ALONE
COMBINED
Clear weather
Good
Excellent
Excellent
Heavy fog + 90° angle
Excellent
Poor
Excellent
Rain + 45° angle
Excellent
Good
Excellent
METHOD 1
Weighted by weather
Bad weather → 70% SAM, 30% BEV
Good weather → 50% SAM, 50% BEV
METHOD 2
Confidence
Weight by each model's own confidence score
COMBINED PROCESSING
Run SAMFusion on each frame
Run BEVFusion on each frame
Combine predictions
Bin by angle + weather
Calculate combined mAP per bin
Notes: Run both models on every frame and combine their predictions. Two weighting methods: weather-based and confidence-based. The table states why the combination should work.

## Slide 4
04 · DELIVERABLES
Heatmaps: angle × weather → mAP
Question: does the combined model outperform both in adverse weather and at high angles?
Heatmap 1 · SAMFusion alone
Heatmap 2 · BEVFusion alone
Heatmap 3 · Combined
0°
45°
90°
180°
CLEAR
mAP
mAP
mAP
mAP
RAIN
mAP
mAP
mAP
mAP
FOG
mAP
mAP
mAP
mAP
NIGHT
mAP
mAP
mAP
mAP
Cells are filled per bin by the Phase 1 runs — select a heatmap above.
PHASE 1
Systematic characterisation using the combined approach
Three heatmaps: SAMFusion alone, BEVFusion alone, combined
Cross-dataset validation
Statistical analysis: does the combined model outperform both in adverse weather and clear conditions?
Answer: here is how the combined approach handles different angles
PHASE 2
Optimisation of combined weighting (if time allows)
Real-world deployment considerations
Notes: Phase 1 delivers three heatmaps and a cross-dataset validation. Click the tabs to show which heatmap is which — the cells are filled by the Phase 1 runs. Phase 2 is optimisation of the ensemble weighting, if time allows.

## Slide 5
05 · CANBUS
Five options for CANBUS integration
OPTION
WHAT IT DOES
1 · Input only
Read vehicle speed, steering angle, acceleration to provide context for detection - improves object classification by understanding vehicle motion.
2 · Output only
Send brake commands to trigger AEB based on detection confidence: detection confidence > threshold → activate AEB via CANBUS.
3 · Full AEB loop
Read vehicle state, then decide AEB trigger based on detection + speed + angle + weather: read speed, brake status and steering from CANBUS; detect objects, confidence, angle and weather; decide the AEB threshold from all factors; write the brake command via CANBUS.
4 · Validation
Use CANBUS data to validate detection logic: braking → detected objects stable ahead; accelerating → detected objects move backward.
5 · Contextual weighting
Use vehicle speed to adjust SAMFusion vs BEVFusion weights: low speed / bad weather → favour SAMFusion; high speed / clear weather → favour BEVFusion.
Notes: Five options for CANBUS integration, from read-only context through the full AEB loop. Ask the supervisor which scope is appropriate.

## Slide 6
06 · CONCLUSION
Combining a robustness specialist with an accuracy specialist
SAMFusion - weather robustness specialist
BEVFusion - accuracy specialist
RESEARCH QUESTION
“How does adverse weather affect LIDAR-camera fusion perfomance across different observations angles, and can combined fusion models improve robustness?”
PHASE 1 DELIVERABLES
Three heatmaps plus cross-dataset validation
Statistical analysis of the combined approach against both models
How the combined approach handles different angles
COMPLETE TECH STACK
Languages & frameworks
Python 3.10+
PyTorch 2.0+
MMDetection3D
ONNX
Dataset tools
nuScenes DevKit
KITTI Tools
Open3D
CARMAKER
Processing & analysis
Pandas
NumPy / SciPy
scikit-learn
Visualisation & tooling
Matplotlib
Plotly
Jupyter
VS Code, Git
Notes: Close on the two model roles, the research question, and the tech stack that supports the work.